## Slide 1: Simulation Block Diagram
Human Controller
Navigation/Sensor Model
Atmospheric Model
Aerodynamics/Thrust Model
Dynamics
Control Surface
Deflections/Throttle
Forces/Moments
True State
Estimated State
Ground Model
Wind/
Density/
Pressure/
Temp
Gravity Force/
True Vector
Forces/Moments
Velocity Vector/Attitude
Guidance Waypoints
Autopilot
Guidance Laws
Waypoint States
Actual Sensors
In Arduino
Estimated State
Serial Out
Serial In
Desired States
(Estimated State)
Optional Controller
Optional Sensors (actual for Arduino only)
Optional Arduino
Visualization

## Slide 2: Capabilities
Autopilot
  Steady level flight
  Coordinated Turns
  Take-off
  Landing
Beginner Mode
  Augmented stability (if needed)
  Out of range turn around
  Anti-stall
  Anti-fall out of sky

## Slide 3: Navigation
Input
  True GPS position/velocity, IMU acceleration/angular rate in body frame, Magnetometer heading
  Add noise
Output: estimated states
  Use Kalman Filter
  Attitude & angular rate from IMU
  Position and velocity from GPS and IMU

## Slide 4: Generate Base Models
Actuator Base Model
Propulsion Base Model
Create Mass Base Model

## Slide 5: Actuator Model
ActuatorTypeBase
  Defines one actuator
  Define keyboard up and keyboard down directions
  Define command location type (keyboard, outside, table)
  Outside commands (from serial or autopilot) can be set using setters
  Set command
    Sets the command from an outside souce
  Update
    Input a command
    Output the position
ActuatorBase
  Define multiple actuator types
  Define Keyboard terminal to pass into ActuatorTypeBase