## Slide 1: Simulation Block Diagram
Human Controller
Navigation/Sensor Model
Atmospheric Model
Aerodynamics/Thrust Model
Dynamics
Control Surface
Deflections/Throttle
Forces/Moments
True State
Estimated State
Ground Model
Wind/
Density/
Pressure/
Temp
Gravity Force/
True Vector
Forces/Moments
Velocity Vector/Attitude
Guidance Waypoints
Autopilot
Guidance Laws
Waypoint States
Actual Sensors
In Arduino
Estimated State
Serial Out
Serial In
Desired States
(Estimated State)
Optional Controller
Optional Sensors (actual for Arduino only)
Optional Arduino
Visualization

## Slide 2: Capabilities
Autopilot
  Steady level flight
  Coordinated Turns
  Take-off
  Landing
Beginner Mode
  Augmented stability (if needed)
  Out of range turn around
  Anti-stall
  Anti-fall out of sky

## Slide 3: Navigation
Input
  True GPS position/velocity, IMU acceleration/angular rate in body frame, Magnetometer heading
  Add noise
Output: estimated states
  Use Kalman Filter
  Attitude & angular rate from IMU
  Position and velocity from GPS and IMU

## Slide 4: Generate Base Models
Actuator Base Model
Propulsion Base Model
Create Mass Base Model

## Slide 5: Actuator Model
ActuatorTypeBase
  Defines one actuator
  Define keyboard up and keyboard down directions
  Define command location type (keyboard, outside, table)
  Outside commands (from serial or autopilot) can be set using setters
  Set command
    Sets the command from an outside souce
  Update
    Input a command
    Output the position
ActuatorBase
  Define multiple actuator types
  Define Keyboard terminal to pass into ActuatorTypeBase

## Slide 6: Equations

## Slide 7: Example Parameters
Variable | Value | Units
Ixx | 0.01122 | 
Iyy | 0.01122 | 
Izz | 0.02199 | 
Length | 0.23 | 
mass | 1.04 | 
Kd (drag coeff=1/2ρA) | 0.82 x 10-5 | 
KH (torque coeff) | 1.40 x 10-7 | 
KT (thrust coeff) | 0.00215 | 
0.00215*0.23/0.01122=0.0004945/0.01122=0.044->wn = 0.22

## Slide 8: Rotations and Definitions
[cos(θ) 0 –sin(θ) ]
RB_NED= [sin(θ)sin(Φ) cos(Φ) cos(θ)sin(Φ)]
[sin(θ)cos(Φ) –sin(Φ) cos(θ)cos(Φ)]
[cos(θ) sin(θ)sin(Φ) sin(θ)cos(Φ)]
RNED_B= [ 0 cos(Φ) –sin(Φ) ]
[–sin(θ) cos(θ)sin(Φ) cos(θ)cos(Φ)]
LL to Body
Body to LL
Body Rate to Euler Rate
θ = L ω
[dΦ/dt] [1 sin(Φ)tan(θ) cos(Φ)tan(θ)] [p]
[dθ/dt ] = [ 0 cos(Φ) –sin(Φ) ] [q]
[dΨ/dt] [0 sin(Φ)sec(θ) cos(Φ)sec(θ)] [r]

## Slide 9: Forces
ΣFLL=RLL_BTB + mg
TB=0i + 0j + -TBk
g=0i + 0j + gk
TB=KT(ω12+ω22+ω32+ω42)
Thrust
Gravity
[cos(θ) sin(θ)sin(Φ) sin(θ)cos(Φ) ] [ 0 ] [0]
ΣFLL= [ 0 cos(Φ) –sin(Φ) ] [ 0 ] + m [0]
[–sin(θ) cos(θ)sin(Φ) cos(θ)cos(Φ)] [-TB] [g]
ΣFLL= maLL= -sin(θ)cos(Φ) TBi + sin(Φ)TBj + mg-cos(θ)cos(Φ)TBk
dVLLx/dt = -sin(θ)cos(Φ) KT(ω12+ω22+ω32+ω42)
dVLLy/dt = sin(Φ) KT(ω12+ω22+ω32+ω42)
dVLLz/dt = mg - cos(θ)cos(Φ) KT(ω12+ω22+ω32+ω42)
ΣFLLx = -sin(θ)cos(Φ) KT(ω12+ω22+ω32+ω42)
ΣFLLy = sin(Φ) KT(ω12+ω22+ω32+ω42)
ΣFLLz = mg - cos(θ)cos(Φ) KT(ω12+ω22+ω32+ω42)

## Slide 10: Moments
ΣMB= [(TB1+TB4)L - (TB2+TB3)L]i +[(TB1+TB2)L - (TB3+TB4)L]j + [(H1+H3) – (H2+H4)]k
Hi=KH ωi2
Rotor Moment
ΣMBx= KT[(ω12 +ω42) - (ω22 +ω32)]L
ΣMBy= KT[(ω12 +ω22) - (ω32 +ω42)]L
ΣMBz= KH[(ω12 +ω32) - (ω22 +ω42)]

## Slide 11: Control Inputs
dT – set throttle command
da – roll command
de – pitch command
dr – yaw command
Rotor | Roll Sign | Pitch Sign | Yaw Sign
1 | + | + | +
2 | - | + | -
3 | - | - | +
4 | + | - | -
dT = ω12 + ω22 + ω32 + ω42
da = (ω12 + ω42) – (ω22 + ω32)
de = (ω12 + ω22) – (ω32 + ω42)
dr = (ω12 + ω32) – (ω22 + ω42)
dT = ω12 + ω22 + ω32 + ω42
da = ω12 - ω22 - ω32 + ω42
de = ω12 + ω22 - ω32 - ω42
dr = ω12 - ω22 + ω32 - ω42
[1 1 1 1] [ω12] [dT]
[1 -1 -1 1] [ω22] = [da]
[1 1 -1 -1] [ω32] [de]
[1 -1 1 -1] [ω42] [dr]

## Slide 12: Control Inputs to Rotor Inputs – Way 1
dT = ω12 + ω22 + ω32 + ω42
da = ω12 - ω22 - ω32 + ω42
de = ω12 + ω22 - ω32 - ω42
dr = ω12 - ω22 + ω32 - ω42
Known: dT, da, de, dr
Unkwon: ω12, ω22, ω32, ω42
[1 1 1 1 ] [ω12] [dT]
[1 -1 -1 1] [ω22] = [da]
[1 1 -1 -1] [ω32] [de]
[1 -1 1 -1] [ω42] [dr]
[1/4 1/4 1/4 1/4 ] [dT] [ω12]
[1/4 -1/4 1/4 -1/4] [da] = [ω22]
[1/4 -1/4 -1/4 1/4] [de] [ω32]
[1/4 1/4 -1/4 -1/4] [dr] [ω42]
ω12 = (dT+da+de+dr)/4
ω22 = (dT-da+de-dr)/4
ω32 = (dT-da-de+dr)/4
ω42 = (dT+da-de-dr)/4
dT = ω12 + ω22 + ω32 + ω42
da = (ω12 + ω42) – (ω22 + ω32)
de = (ω12 + ω22) – (ω32 + ω42)
dr = (ω12 + ω32) – (ω22 + ω42)
->
->

## Slide 13: Control Inputs to Rotor Inputs – Way 2
dT+da+de+dr = 4ω12 -> ω12 = (dT+da+de+dr )/4 -> dT+da+de+dr ≥ 0
dT+da-de-dr = 4ω42 -> ω42 = (dT+da-de-dr )/4 -> dT+da ≥ de+dr
dT-da-de+dr = 4ω32 -> ω32 = (dT-da-de+dr )/4 -> dT+dr ≥ da+de
dT-da+de-dr = 4ω22 -> ω22 = (dT-da+de-dr )/4 -> dT+de ≥ da+dr
dT = ω12 + ω22 + ω32 + ω42
da = ω12 - ω22 - ω32 + ω42
de = ω12 + ω22 - ω32 - ω42
dr = ω12 - ω22 + ω32 - ω42
Known: dT, da, de, dr
Unkwon: ω12, ω22, ω32, ω42
dT = ω12 + ω22 + ω32 + ω42
da = (ω12 + ω42) – (ω22 + ω32)
de = (ω12 + ω22) – (ω32 + ω42)
dr = (ω12 + ω32) – (ω22 + ω42)
->
->

## Slide 14: Control Input Contraints
dT+da+de+dr ≥ 0
dT+da-de-dr ≥ 0
dT-da-de+dr ≥ 0
dT-da+de-de ≥ 0
dT+da+de+dr ≤ 4ωmax2
dT+da-de-dr ≤ 4ωmax2
dT-da-de+dr ≤ 4ωmax2
dT-da+de-de ≤ 4ωmax2
da = de = dr = x dT
dT + 3x dT ≥ 0
dT - 2x dT ≥ 0
dT - 2x dT ≥ 0
dT - 2x dT ≥ 0
1 ≥-3x
1 ≥ 2x
x ≥-1/3
x ≤ 1/2
-1/3 dT ≤ da = de = dr ≤ 1/2dT
dMax = 4ωmax2
dT + 3x dT ≤ dMax
dT - 2x dT ≤ dMax
dT - 2x dT ≤ dMax
dT - 2x dT ≤ dMax
dT + 3x dT ≤ dMax
dT - 2x dT ≤ dMax
x ≤ (dMax – dT)/(3dT)
x ≥ (dT – dMax)/(2dT)
(dT – dMax)/(2dT) dT ≤ da = de = dr ≤ (dMax – dT)/(3dT) dT
-(dMax - dT )/2 ≤ da = de = dr ≤ (dMax – dT)/3

## Slide 15: Control Input Contraints
da < 0.5*dT
da > -1/3*dT
min dT when roll, pitch, or yaw is desired. Greater of
2*dmax
-3*dmax
At all times dTmin < dTo, and dTmax > dTo
Must be less than
dTo to retain velocity control

## Slide 16: Throttle to RPM to Throttle
PWM In | dT | ω = sqrt(dT/4) | RPM | PWM = (ω – b)/m | PWM Cmd
1000 | 0 |  | 0 |  | 1000
1100 |  |  |  |  | 1100
1200 | 4*ωmin2 | ω = sqrt(4*ωmin2/4) | ωmin |  | 1200
2000 | 4*ωmax2 |  | ωmax |  | 2000

## Slide 17: Throttle to RPM
Throttle % | PWM | RPM | Comment
0 | 1,000 | 0 | 
minThrottle>0 | minPWM>1,000 | minRPM | No RPM below 10% throttle
maxThrottle | maxPWM=2,000 | maxRPM | Linear to max RPM
if (Throttle < minThrottle) {
RPM = 0;
}
else {
RPM = m*Throttle + b;
}

## Slide 18: Controller Inputs to PWM
ω12 = (dT+da+de+dr)/4
ω22 = (dT-da+de-dr)/4
ω32 = (dT-da-de+dr)/4
ω42 = (dT+da-de-dr)/4
ωi=m*Throttlei + b
if (ωi < rpmMin) {
Throttlei = minPWM
}
else {
Throttlei = (sqrt(ωi2)-b)/m
}

## Slide 19: Control Architecture
Control Roll, Pitch, YawRate inner loop
Control VLLx, VLLy, VLLz outer loop
VLLxcmd -> Pitchcmd -> de
VLLycmd -> Rollcmd -> da
VLLzcmd -> dT
YawRatecmd->dr
Inner loop 4x faster than outer loop

## Slide 20: Forces, Moments, and Control Inputs
ΣFLLx = m(dVLLx/dt) = -sin(θ)cos(Φ) KTdT
ΣFLLy = m(dVLLy/dt) = sin(Φ) KTdT
ΣFLLz = m(dVLLz/dt) = mg - cos(θ)cos(Φ) KTdT
ΣMBx= Ixx(dp/dt)+qr(Izz-Iyy) = KTLda
ΣMBy= Iyy(dq/dt)+pr(Ixx-Izz) = KTLde
ΣMBz= Izz(dr/dt)+pq(Iyy-Ixx) = KHdr
dVLLx/dt = -1/m*sin(θ)cos(Φ) KTdT
dVLLy/dt = 1/m*sin(Φ) KTdT
dVLLz/dt = g – 1/m*cos(θ)cos(Φ) KTdT
dp/dt = (KTL/Ixx) da - qr(Izz-Iyy)/Ixx
dq/dt = (KTL/Iyy) de - pr(Ixx-Izz) /Iyy
dr/dt = (KH/Izz) dr - pq(Iyy-Ixx)/Izz
[dΦ/dt] [1 sin(Φ)tan(θ) cos(Φ)tan(θ)] [p]
[dθ/dt ] = [ 0 cos(Φ) –sin(Φ) ] [q]
[dΨ/dt] [0 sin(Φ)sec(θ) cos(Φ)sec(θ)] [r]

## Slide 21: Linearization Assumptions
x = [VLLx, VLLy, VLLz, θ, Φ, p, q, r]
u = [dT, da, de, dr]
Linearize about hover
  x = [0, 0, 0, 0, 0, 0, 0, 0]
  u = [mg/KT, 0, 0, 0]
  dT=mg/KT is the dT for constant altitude

## Slide 22: Linearization
dVLLx/dt = -(KTdTo/m)θ
dVLLy/dt = (KTdTo/m)Φ
dVLLz/dt = -(KT/m)ΔdT
dΦ/dt = p
dθ/dt = q
dψ/dt = r
dp/dt = d2Φ/dt2 = KTL/Ixxda
dq/dt = d2θ/dt2 = KTL/Iyyde
dr/dr =d2ψ/dt2 = KH/Izz dr

## Slide 23: Vx Control Loops
dVLLx/dt = (-KTdTo/m)θ
d2θ/dt2 = KTL/Iyyde
sVLLx(s) = -Kvxθ(s)
s2θ(s) = Kθde(s)
Kvx = KTdTo/m
Kθ = KTL/Iyy
Pvx(s) =VLLx(s)/θ(s) = -Kvx/s
Pθ(s) = θ(s)/de(s) = Kθ/s2
Cθ(s)
Cvx(s)
Kθ/s2
-Kvx/s
Vxcmd
+
-
Vxe
θcmd
+
-
θe
de
θ
Vx
Pθ(s)
Pvx(s)
Cθ(s)
-Kvx/s
+
-
Vxe
θcmd
θ
Vx
Hθ(s)
Vxcmd

## Slide 24: Vx Inner Pitch Loop
Cvx(s)
Kθ/s2
θcmd
+
-
θe
de
θ
G(s) = θ(s)/θe(s) = Cvx(s) Pθ(s)
PD Controller
de(s) = kp*θe(s)+s*kd*θe(s)
Cvx(s) = de(s)/θe(s) = kp+s*kd
G(s) =Cvx(s)Pθ(s) = kθ(kp+s*kd)/s2
H(s) = θ(s)/θcmd(s) = G(s)/(1+G(s)) = (kθ*kd*s+kθ*kp) / (s2+kθ*kd*s+kθ*kp)
Steady State Error
θe(s) = θcmd(s)/(1+G(s)) = s2θcmd(s)/(s2+kθkds+kθkp)
Steady state error = 0 for impulse, step, and ramp inputs

## Slide 25: Vx Inner Loop Response
H(s) = θ(s)/θcmd(s) = G(s)/(1+G(s)) = (kθ*kd*s+kθ*kp) / (s2+kθ*kd*s+kθ*kp)
wn = 80 * 2 * pi = 502.4
zeta = 1
s2+kθ*kd*s+kθ*kp = s2 + 2*zeta*wn*s + wn2
kp = wn2/kθ = 148,473,976
kd = 2*zeta*wn/kθ = 591,058.8
Kθ = KTL/Iyy
KT = Tmax/(maxrpm2) = 4.22/(rad(64402)) = 0.000334
L = 0.1
Iyy = 0.0196
Kθ = 0.0017

## Slide 26: Vy Control Loops

## Slide 27: Vz Control Loop
CT(s)
-Kvz/s
+
-
ΔdTcmd
Vz
Vzcmd
dVLLz/dt = (-KT/m)ΔdT
sVLLz(s) = -KvzΔdT(s)
Kvz = KT/m
Pvz(s) =VLLz(s)/ΔdT (s) = -Kvz/s
P Controller
ΔdT(s) = kp*Vze(s) -> Cvz(s) = ΔdT(s)/Vze (s) = kp
G(s) =Cvz(s)PT(s) = -kpKvz/s
H(s) = Vz(s)/Vzcmd(s) = G(s)/(1+G(s)) = (-kpKvz) / (s-kpKvz)
Steady State Error
Vze(s) = Vzcmd(s)/(1+G(s)) = sVzcmd(s)/(s-kpKvz)
Steady state error = 0 for impulse and step inputs, -1/kpKvz error for ramp input
Vze

## Slide 28: Yaw Rate Control Loop
CT(s)
-Kvz/s
+
-
ΔdTcmd
Vz
Vzcmd
dVLLz/dt = (-KT/m)ΔdT
sVLLz(s) = -KvzΔdT(s)
Kvz = KT/m
Pvz(s) =VLLz(s)/ΔdT (s) = -Kvz/s
P Controller
ΔdT(s) = kp*Vze(s) -> Cvz(s) = ΔdT(s)/Vze (s) = kp
G(s) =Cvz(s)PT(s) = -kpKvz/s
H(s) = Vz(s)/Vzcmd(s) = G(s)/(1+G(s)) = (-kpKvz) / (s-kpKvz)
Steady State Error
Vze(s) = Vzcmd(s)/(1+G(s)) = sVzcmd(s)/(s-kpKvz)
Steady state error = 0 for impulse and step inputs, -1/kpKvz error for ramp input
Vze

## Slide 29: Yaw Rate Loop Response
H(s) = r(s)/rcmd(s) = G(s)/(1+G(s)) = (kp*kr)/(s+kp*kr)
wn = 1500 * 2 * pi = 9,420
wn = kp*kr
kp = wn/kr = 248,680,042
kr = KH/Izz
KH = Q*KT = 0.003*0.000334 = 0.000001
Izz= 0.0264
kr = 0.00003788