## Slide 1: Simulation Block Diagram
Human Controller
Navigation/Sensor Model
Atmospheric Model
Aerodynamics/Thrust Model
Dynamics
Control Surface
Deflections/Throttle
Forces/Moments
True State
Estimated State
Ground Model
Wind/
Density/
Pressure/
Temp
Gravity Force/
True Vector
Forces/Moments
Velocity Vector/Attitude
Guidance Waypoints
Autopilot
Guidance Laws
Waypoint States
Actual Sensors
In Arduino
Estimated State
Serial Out
Serial In
Desired States
(Estimated State)
Optional Controller
Optional Sensors (actual for Arduino only)
Optional Arduino
Visualization

## Slide 2: Capabilities
Autopilot
  Steady level flight
  Coordinated Turns
  Take-off
  Landing
Beginner Mode
  Augmented stability (if needed)
  Out of range turn around
  Anti-stall
  Anti-fall out of sky

## Slide 3: Navigation
Input
  True GPS position/velocity, IMU acceleration/angular rate in body frame, Magnetometer heading
  Add noise
Output: estimated states
  Use Kalman Filter
  Attitude & angular rate from IMU
  Position and velocity from GPS and IMU

## Slide 4: Generate Base Models
Actuator Base Model
Propulsion Base Model
Create Mass Base Model

## Slide 5: Actuator Model
ActuatorTypeBase
  Defines one actuator
  Define keyboard up and keyboard down directions
  Define command location type (keyboard, outside, table)
  Outside commands (from serial or autopilot) can be set using setters
  Set command
    Sets the command from an outside souce
  Update
    Input a command
    Output the position
ActuatorBase
  Define multiple actuator types
  Define Keyboard terminal to pass into ActuatorTypeBase

## Slide 6: IMU Uncertainty Sources

## Slide 7: IMU Quanitzation Errors
Error = val – floor(val*LSB)/LSB
  Cannot sense decimal places of val*LSB, only every integer
Minimum sensed value
  val*LSB = 1
  min_val = 1/LSB
  Given val = 0, error can be up to 1/LSB
Next sensed value
  val*LSB = 2
Zero Error when val is a multiple of LSB
Maximum Error is 1/LSB

## Slide 8: Equations

## Slide 9: Example Parameters
Variable | Value | Units
Ixx | 0.01122 | 
Iyy | 0.01122 | 
Izz | 0.02199 | 
Length | 0.23 | 
mass | 1.04 | 
Kd (drag coeff=1/2ρA) | 0.82 x 10-5 | 
KH (torque coeff) | 1.40 x 10-7 | 
KT (thrust coeff) | 0.00215 | 
0.00215*0.23/0.01122=0.0004945/0.01122=0.044->wn = 0.22

## Slide 10: Rotations and Definitions
[cos(θ) 0 –sin(θ) ]
RB_NED= [sin(θ)sin(Φ) cos(Φ) cos(θ)sin(Φ)]
[sin(θ)cos(Φ) –sin(Φ) cos(θ)cos(Φ)]
[cos(θ) sin(θ)sin(Φ) sin(θ)cos(Φ)]
RNED_B= [ 0 cos(Φ) –sin(Φ) ]
[–sin(θ) cos(θ)sin(Φ) cos(θ)cos(Φ)]
LL to Body
Body to LL
Body Rate to Euler Rate
θ = L ω
[dΦ/dt] [1 sin(Φ)tan(θ) cos(Φ)tan(θ)] [p]
[dθ/dt ] = [ 0 cos(Φ) –sin(Φ) ] [q]
[dΨ/dt] [0 sin(Φ)sec(θ) cos(Φ)sec(θ)] [r]

## Slide 11: Forces
ΣFLL=RLL_BTB + mg
TB=0i + 0j + -TBk
g=0i + 0j + gk
TB=KT(ω12+ω22+ω32+ω42)
Thrust
Gravity
[cos(θ) sin(θ)sin(Φ) sin(θ)cos(Φ) ] [ 0 ] [0]
ΣFLL= [ 0 cos(Φ) –sin(Φ) ] [ 0 ] + m [0]
[–sin(θ) cos(θ)sin(Φ) cos(θ)cos(Φ)] [-TB] [g]
ΣFLL= maLL= -sin(θ)cos(Φ) TBi + sin(Φ)TBj + mg-cos(θ)cos(Φ)TBk
dVLLx/dt = -sin(θ)cos(Φ) KT(ω12+ω22+ω32+ω42)
dVLLy/dt = sin(Φ) KT(ω12+ω22+ω32+ω42)
dVLLz/dt = mg - cos(θ)cos(Φ) KT(ω12+ω22+ω32+ω42)
ΣFLLx = -sin(θ)cos(Φ) KT(ω12+ω22+ω32+ω42)
ΣFLLy = sin(Φ) KT(ω12+ω22+ω32+ω42)
ΣFLLz = mg - cos(θ)cos(Φ) KT(ω12+ω22+ω32+ω42)

## Slide 12: Moments
ΣMB= [(TB1+TB4)L - (TB2+TB3)L]i +[(TB1+TB2)L - (TB3+TB4)L]j + [(H1+H3) – (H2+H4)]k
Hi=KH ωi2
Rotor Moment
ΣMBx= KT[(ω12 +ω42) - (ω22 +ω32)]L
ΣMBy= KT[(ω12 +ω22) - (ω32 +ω42)]L
ΣMBz= KH[(ω12 +ω32) - (ω22 +ω42)]

## Slide 13: Control Inputs
dT – set throttle command
da – roll command
de – pitch command
dr – yaw command
Rotor | Roll Sign | Pitch Sign | Yaw Sign
1 | + | + | +
2 | - | + | -
3 | - | - | +
4 | + | - | -
dT = ω12 + ω22 + ω32 + ω42
da = (ω12 + ω42) – (ω22 + ω32)
de = (ω12 + ω22) – (ω32 + ω42)
dr = (ω12 + ω32) – (ω22 + ω42)
dT = ω12 + ω22 + ω32 + ω42
da = ω12 - ω22 - ω32 + ω42
de = ω12 + ω22 - ω32 - ω42
dr = ω12 - ω22 + ω32 - ω42
[1 1 1 1] [ω12] [dT]
[1 -1 -1 1] [ω22] = [da]
[1 1 -1 -1] [ω32] [de]
[1 -1 1 -1] [ω42] [dr]

## Slide 14: Control Inputs to Rotor Inputs – Way 1
dT = ω12 + ω22 + ω32 + ω42
da = ω12 - ω22 - ω32 + ω42
de = ω12 + ω22 - ω32 - ω42
dr = ω12 - ω22 + ω32 - ω42
Known: dT, da, de, dr
Unkwon: ω12, ω22, ω32, ω42
[1 1 1 1 ] [ω12] [dT]
[1 -1 -1 1] [ω22] = [da]
[1 1 -1 -1] [ω32] [de]
[1 -1 1 -1] [ω42] [dr]
[1/4 1/4 1/4 1/4 ] [dT] [ω12]
[1/4 -1/4 1/4 -1/4] [da] = [ω22]
[1/4 -1/4 -1/4 1/4] [de] [ω32]
[1/4 1/4 -1/4 -1/4] [dr] [ω42]
ω12 = (dT+da+de+dr)/4
ω22 = (dT-da+de-dr)/4
ω32 = (dT-da-de+dr)/4
ω42 = (dT+da-de-dr)/4
dT = ω12 + ω22 + ω32 + ω42
da = (ω12 + ω42) – (ω22 + ω32)
de = (ω12 + ω22) – (ω32 + ω42)
dr = (ω12 + ω32) – (ω22 + ω42)
->
->

## Slide 15: Control Inputs to Rotor Inputs – Way 2
dT+da+de+dr = 4ω12 -> ω12 = (dT+da+de+dr )/4 -> dT+da+de+dr ≥ 0
dT+da-de-dr = 4ω42 -> ω42 = (dT+da-de-dr )/4 -> dT+da ≥ de+dr
dT-da-de+dr = 4ω32 -> ω32 = (dT-da-de+dr )/4 -> dT+dr ≥ da+de
dT-da+de-dr = 4ω22 -> ω22 = (dT-da+de-dr )/4 -> dT+de ≥ da+dr
dT = ω12 + ω22 + ω32 + ω42
da = ω12 - ω22 - ω32 + ω42
de = ω12 + ω22 - ω32 - ω42
dr = ω12 - ω22 + ω32 - ω42
Known: dT, da, de, dr
Unkwon: ω12, ω22, ω32, ω42
dT = ω12 + ω22 + ω32 + ω42
da = (ω12 + ω42) – (ω22 + ω32)
de = (ω12 + ω22) – (ω32 + ω42)
dr = (ω12 + ω32) – (ω22 + ω42)
->
->

## Slide 16: Control Input Contraints
dT+da+de+dr ≥ 0
dT+da-de-dr ≥ 0
dT-da-de+dr ≥ 0
dT-da+de-de ≥ 0
dT+da+de+dr ≤ 4ωmax2
dT+da-de-dr ≤ 4ωmax2
dT-da-de+dr ≤ 4ωmax2
dT-da+de-de ≤ 4ωmax2
da = de = dr = x dT
dT + 3x dT ≥ 0
dT - 2x dT ≥ 0
dT - 2x dT ≥ 0
dT - 2x dT ≥ 0
1 ≥-3x
1 ≥ 2x
x ≥-1/3
x ≤ 1/2
-1/3 dT ≤ da = de = dr ≤ 1/2dT
dMax = 4ωmax2
dT + 3x dT ≤ dMax
dT - 2x dT ≤ dMax
dT - 2x dT ≤ dMax
dT - 2x dT ≤ dMax
dT + 3x dT ≤ dMax
dT - 2x dT ≤ dMax
x ≤ (dMax – dT)/(3dT)
x ≥ (dT – dMax)/(2dT)
(dT – dMax)/(2dT) dT ≤ da = de = dr ≤ (dMax – dT)/(3dT) dT
-(dMax - dT )/2 ≤ da = de = dr ≤ (dMax – dT)/3

## Slide 17: Control Input Contraints
da < 0.5*dT
da > -1/3*dT
min dT when roll, pitch, or yaw is desired. Greater of
2*dmax
-3*dmax
At all times dTmin < dTo, and dTmax > dTo
Must be less than
dTo to retain velocity control

## Slide 18: Throttle to RPM to Throttle
PWM In | dT | ω = sqrt(dT/4) | RPM | PWM = (ω – b)/m | PWM Cmd
1000 | 0 |  | 0 |  | 1000
1100 |  |  |  |  | 1100
1200 | 4*ωmin2 | ω = sqrt(4*ωmin2/4) | ωmin |  | 1200
2000 | 4*ωmax2 |  | ωmax |  | 2000
dMin = 4*ωmin2 = 4*(500*2*3.14/60)2 = 10,955.11
dMax = 4*ωmax2 = 4*(6440*2*3.14/60)2 = 1,817,391.58

## Slide 19: Throttle to RPM
Throttle % | PWM | RPM | Comment
0 | 1,000 | 0 | 
minThrottle>0 | minPWM>1,000 | minRPM | No RPM below 10% throttle
maxThrottle | maxPWM=2,000 | maxRPM | Linear to max RPM
if (Throttle < minThrottle) {
RPM = 0;
}
else {
RPM = m*Throttle + b;
}

## Slide 20: Controller Inputs to PWM
ω12 = (dT+da+de+dr)/4
ω22 = (dT-da+de-dr)/4
ω32 = (dT-da-de+dr)/4
ω42 = (dT+da-de-dr)/4
ωi=m*Throttlei + b
if (ωi < rpmMin) {
Throttlei = minPWM
}
else {
Throttlei = (sqrt(ωi2)-b)/m
}

## Slide 21: Control Architecture
Control Roll, Pitch, YawRate inner loop
Control VLLx, VLLy, VLLz outer loop
VLLxcmd -> Pitchcmd -> de
VLLycmd -> Rollcmd -> da
VLLzcmd -> dT
YawRatecmd->dr
Inner loop 4x faster than outer loop

## Slide 22: Forces, Moments, and Control Inputs
ΣFLLx = m(dVLLx/dt) = -sin(θ)cos(Φ) KTdT
ΣFLLy = m(dVLLy/dt) = sin(Φ) KTdT
ΣFLLz = m(dVLLz/dt) = mg - cos(θ)cos(Φ) KTdT
ΣMBx= Ixx(dp/dt)+qr(Izz-Iyy) = KTLda
ΣMBy= Iyy(dq/dt)+pr(Ixx-Izz) = KTLde
ΣMBz= Izz(dr/dt)+pq(Iyy-Ixx) = KHdr
dVLLx/dt = -1/m*sin(θ)cos(Φ) KTdT
dVLLy/dt = 1/m*sin(Φ) KTdT
dVLLz/dt = g – 1/m*cos(θ)cos(Φ) KTdT
dp/dt = (KTL/Ixx) da - qr(Izz-Iyy)/Ixx
dq/dt = (KTL/Iyy) de - pr(Ixx-Izz) /Iyy
dr/dt = (KH/Izz) dr - pq(Iyy-Ixx)/Izz
[dΦ/dt] [1 sin(Φ)tan(θ) cos(Φ)tan(θ)] [p]
[dθ/dt ] = [ 0 cos(Φ) –sin(Φ) ] [q]
[dΨ/dt] [0 sin(Φ)sec(θ) cos(Φ)sec(θ)] [r]

## Slide 23: Linearization Assumptions
x = [VLLx, VLLy, VLLz, θ, Φ, p, q, r]
u = [dT, da, de, dr]
Linearize about hover
  x = [0, 0, 0, 0, 0, 0, 0, 0]
  u = [mg/KT, 0, 0, 0]
  dT=mg/KT is the dT for constant altitude

## Slide 24: Linearization
dVLLx/dt = -(KTdTo/m)θ
dVLLy/dt = (KTdTo/m)Φ
dVLLz/dt = -(KT/m)ΔdT
dΦ/dt = p
dθ/dt = q
dψ/dt = r
dp/dt = d2Φ/dt2 = KTL/Ixxda
dq/dt = d2θ/dt2 = KTL/Iyyde
dr/dt =d2ψ/dt2 = KH/Izz dr

## Slide 25: Vx Control Loops
dVLLx/dt = (-KTdTo/m)θ
d2θ/dt2 = KTL/Iyyde
sVLLx(s) = -Kvxθ(s)
s2θ(s) = Kθde(s)
Kvx =- KTdTo/m
Kθ = KTL/Iyy
Pvx(s) =VLLx(s)/θ(s) = Kvx/s
Pθ(s) = θ(s)/de(s) = Kθ/s2
Cθ(s)
Cvx(s)
Kθ/s2
Kvx/s
Vxcmd
+
-
Vxe
θcmd
+
-
θe
de
θ
Vx
Pθ(s)
Pvx(s)
Cθ(s)
Kvx/s
+
-
Vxe
θcmd
θ
Vx
Hθ(s)
Vxcmd

## Slide 26: Vx Inner Pitch Loop
Cvx(s)
Kθ/s2
θcmd
+
-
θe
de
θ
G(s) = θ(s)/θe(s) = Cvx(s) Pθ(s)
P Controller
de(s) = kp*θe(s)+s*kd*θe(s)
Cvx(s) = de(s)/θe(s) = kp+s*kd
G(s) =Cvx(s)Pθ(s) = kθ(kp+s*kd)/s2
H(s) = θ(s)/θcmd(s) = G(s)/(1+G(s)) = (kθ*kd*s+kθ*kp) / (s2+kθ*kd*s+kθ*kp)
Steady State Error
θe(s) = θcmd(s)/(1+G(s)) = s2θcmd(s)/(s2+kθkds+kθkp)
Steady state error = 0 for impulse, step, and ramp inputs

## Slide 27: Vx Inner Loop Response
H(s) = θ(s)/θcmd(s) = G(s)/(1+G(s)) = (kθ*kd*s+kθ*kp) / (s2+kθ*kd*s+kθ*kp)
wn = 80 * 2 * pi = 502.4
zeta = 1
s2+kθ*kd*s+kθ*kp = s2 + 2*zeta*wn*s + wn2
kp = wn2/kθ = 148,473,976
kd = 2*zeta*wn/kθ = 591,058.8
Kθ = KTL/Iyy
KT = Tmax/(maxrpm2) = 4.22/(rad(64402)) = 0.000334
L = 0.1
Iyy = 0.0196
Kθ = 0.0017

## Slide 28: Vx/Vy Outer Pitch Loop
G(s) = Vx(s)/Vxe(s) = Cθ(s) Hθ(s) Pvx(s)
PI Controller
θcmd(s) = kp*Vxe(s)
Cθ(s) = θcmd (s)/Vxe(s) = kp
G(s) =Cθ(s)Pvx(s) = kpKvx/s
H(s) = Vx(s)/Vxcmd(s) = G(s)/(1+G(s)) = kpKvx/ (s+kpKvx)
Steady State Error
Vxe(s) = Vxcmd(s)/(1+G(s)) = sVxcmd(s)/(s+kpKvx)
Steady state error = 0 for impulse and step inputs, 1/kpKvx error for ramp input
Cθ(s)
Kvx/s
+
-
Vxe
θcmd
θ
Vx
Hθ(s)
Vxcmd

## Slide 29: Vx/Vy Outer Loop Response
H(s) = Vx(s)/Vxcmd(s) = G(s)/(1+G(s)) = (kpKvx) / (s+kpKvx)
wn = kp*Kvx
kp = wn/Kvx
Kvx = - KTdTo/m
KT = Tmax/(maxrpm2)
m = 0.5

## Slide 30: Vx/Vy PI Outer Pitch Loop
G(s) = Vx(s)/Vxe(s) = Cθ(s) Hθ(s) Pvx(s)
PI Controller
θcmd(s) = (kp + ki/s)*Vxe(s)
Cθ(s) = θcmd (s)/Vxe(s) = kp + ki/s
G(s) =Cθ(s)Pvx(s) = kpKvx/s + kiKvx/s2
H(s) = Vx(s)/Vxcmd(s) = G(s)/(1+G(s)) = (kpKvxs + kiKvx)/ (s2+kpKvxs + kiKvx)
Steady State Error
Vxe(s) = Vxcmd(s)/(1+G(s)) =Vxcmd(s) s2/(s2+kpKvxs + kiKvx)
Steady state error = 0 for impulse, step inputs, and ramp input
Cθ(s)
Kvx/s
+
-
Vxe
θcmd
θ
Vx
Hθ(s)
Vxcmd

## Slide 31: Vx/Vy PI Outer Loop Response
H(s) = Vx(s)/Vxcmd(s) = G(s)/(1+G(s)) = )kpKvxs + kiKvx)/ (s2+kpKvxs + kiKvx)
wn = ki*Kvx -> ki = wn/Kvx
2*zeta*wn = kpKvxx -> kp = 2*zeta*wn/Kvx
Kvx = - KTdTo/m
KT = Tmax/(maxrpm2)
m = 0.5

## Slide 32: Vz Control Loop
CT(s)
Kvz/s
+
-
ΔdTcmd
Vz
Vzcmd
dVLLz/dt = (-KT/m)ΔdT
sVLLz(s) = KvzΔdT(s)
Kvz = -KT/m
Pvz(s) =VLLz(s)/ΔdT (s) = Kvz/s
P Controller
ΔdT(s) = kp*Vze(s) -> Cvz(s) = ΔdT(s)/Vze (s) = kp
G(s) =Cvz(s)PT(s) = kpKvz/s
H(s) = Vz(s)/Vzcmd(s) = G(s)/(1+G(s)) = (kpKvz) / (s+kpKvz)
Steady State Error
Vze(s) = Vzcmd(s)/(1+G(s)) = sVzcmd(s)/(s+kpKvz)
Steady state error = 0 for impulse and step inputs, 1/kpKvz error for ramp input
Vze

## Slide 33: Vz Loop Response
H(s) = Vz(s)/Vzcmd(s) = G(s)/(1+G(s)) = (kpKvz) / (s+kpKvz)
wn = 2 * 2 * pi = 12.56
wn = kp*Kvz
kp = wn/Kvz = -676,085.077
Kvz = -KT/m
KT = Tmax/(maxrpm2) = 4.22/(rad(64402)) = 0.0000092786219540526721
m = 0.5
Kvz = -0.00001858

## Slide 34: Vz PI Control Loop
Same as Vx/Vy but with Kvz

## Slide 35: Altitude Control Loop
Ch(s)
-1/s
+
-
VLLzcmd
Vz
hcmd
dh/dt = -VLLz
sh (s) = -VLLz(s)
Ph(s) =h (s)/VLLz(s) = -1/s
P Controller
VLLzcmd(s) = kp*he(s) -> Ch(s) = VLLzcmd (s)/he (s) = kp
G(s) =Ch(s)Ph(s) = -kp/s
H(s) = h(s)/hcmd(s) = G(s)/(1+G(s)) = (-kp) / (s-kp)
Steady State Error
he(s) = hcmd(s)/(1+G(s)) = shcmd(s)/(s-kp)
Steady state error = 0 for impulse and step inputs, -1/kp error for ramp input
he
Hvz(s)
h

## Slide 36: Altitude Loop Response
H(s) = h(s)/hcmd(s) = G(s)/(1+G(s)) = (-kp) / (s-kp)
wn = 1.0* pi = 3.14
wn = -kp
kp = -wn = -3.14

## Slide 37: Yaw Rate Control Loop
Cr(s)
Kr/s
+
-
drcmd
r
rcmd
dr/dt = (KH/Izz)dr
sr(s) = (KH/Izz)dr(s)
Kr = KH/Izz
Pr(s) =r(s)/dr (s) Kr/s
P Controller
dr(s) = kp*re(s) -> Cr(s) = dr(s)/re (s) = kp
G(s) =Cr(s)Pr(s) = kpKr/s
H(s) = r(s)/rcmd(s) = G(s)/(1+G(s)) = (kpKr) / (s+kpKr)
Steady State Error
re(s) = rcmd(s)/(1+G(s)) = srcmd(s)/(s+kpKr)
Steady state error = 0 for impulse and step inputs, 1/kpKr error for ramp input
re

## Slide 38: Yaw Rate Loop Response
H(s) = r(s)/rcmd(s) = G(s)/(1+G(s)) = (kp*kr)/(s+kp*kr)
wn = 20 * 2 * pi = 125.6
wn = kp*kr
kp = wn/kr =3,315,733.9
kr = KH/Izz
KH = Q*KT = 0.003*0.000334 = 0.000001
Izz= 0.0264
kr = 0.00003788

## Slide 39: Kalman Filter

## Slide 40: Navigation Corrections
Ground Align
  Only to calibrate before GPS ready and for first-time on ground only
  Position and Velocity is Zero
GPS Align
  Position update
  Velocity update

## Slide 41: Navigation Position
North, East, Altitude
All zeros at start point on ground
Barometer
  Zero on ground
    Take first measurement as zero
    Take average of 5 measurements as zero
GPS
  Take initial ECEF Position as zero
  Take average of 5 ECEF Positions as zero
Three Modes
  Non-GPS
    Do not wait for GPS to allow take-off
    Use GPS once available
    Always in attitude control
  Non-GPS Takeoff
    Do not wait for GPS to allow take-off
    Use GPS once available
    Velocity control with GPS, attitude control without GPS
  GPS Takeoff
    Need GPS to allow take-off
    Ok if loose GPS in flight
    Velocity control with GPS, attitude control without GPS

## Slide 42: GPS
Messags
Nav

## Slide 43: Setup
GPS GND – GND
GPS VCC – 5V
GPS RX - Digital 3 (MCU TX)
GPS TX – Digital 2 (MCU RX)
GPS Pins (Looking at GPS Left to Right)
  PPS
  TX
  RX
  GND
  VCC

## Slide 44: GPS NEO-6M Configuration
Messages received (UBX-CFG-MSG)
  Sect 31.9, Page 117/210
  Send configuration message at startup
Timepulse (UBX-TIM-TP)
Power Mode (UBX-CFG-RXM)
  Eco Mode
    Full power during acquisition
    Less power once tracking
  Power Save Mode
    Reduced power
Config acknowledgement
  Awknowldege configuration, ACK-ACK
  Not awknowledge, ACK-NAK

## Slide 45: GPS NEO-6M Nav
Nav (0x01)
Periodic
Can also be polled
NAV-POSLLH (0x01 0x02)– position
NAV-VELNED (0x01 0x12) – velocity
NAV-STATUS (0x01 0x03) – fix status
NAV-DOP (0x01 0x04) – Dillution of Percision
NAV-SOL (0x01 0x06)

## Slide 46: GPS NEO-6M Aid
Teensy EEOPROM: 1080 bytes
AID-ALM: 0x0B 0x30
  No data: get all SV almanac data
  1 byte for svid: alamanc data for 1 satellite
  If Week is zero, no almanac for this satellite
  Use NAV-SVINFO or RXM-SVSI for almanac availability
  Each Almanac is 40bytes. Store first 12 in EEPROM
AID-DATA: 0x0B 0x10
  Receive AID-INI, AID-HUI, AID-EPH, and AID-ALM
AID-EPH: 0x0B 0x31
  Ephemeris
  104 bytes. Store first 12 in EEPROM
AID-HUI: 0x0B 0x02
  GPS Health
AID-INI: 0x0B 0x01

## Slide 47: GPS Aid
Use CFG MSG to configure AID-REQ
  Monitor for AID-DATA, if sent, GPS need position and time

## Slide 48: Teensy 4.0 EEPROM
1080 bytes
HUI = 72 bytes
EPH = 104 bytes
ALM = 40 bytes
INI = 48 bytes

## Slide 49: Hardware

## Slide 50: Hardware Power
Hardware | Radio Frequency | Voltage | Current (Peak) | Max Power Draw | IO | Pins
GPS-Neo6m | 1.575 GHz | 2.7-3.6V | 50mA | (3.3x0.05) 0.165W | UART | 
APC220 Radio | 431-478 MHz | 3.3-5.5V | 25-35mA | (3.3x0.035) 0.1155W | UART | 
HC05 BLE | 2.4 GHz | 3.3V | 50mA | (3.3x0.05) 0.165W | UART | 
IMU GY-521 |  | 2.375-3.46V | 3.8mA | (3.3x0.038) 0.1254W | I2C | 
Baro BMP180 |  | 1.8-3.6V | 0.032 mA (0.65mA) | (3.3x0.0032) 0.01056W | I2C | 
Teensy 4.0 |  | 3.6-5.5V | 250mA | (3.3x0.25) 0.825W |  | 
Arduino Nano |  | 7V-12V | 250mA | (5x0.25) 1.25W |  | 
3.3V Regulator |  | 4.75-12 | 800mA output |  |  | 
ESC (x4) |  | 7.4-22.2 in, 5V out | 2A output |  |  | 
Motor (x4) |  | 7-12 |  |  |  | 
Drone Power = 1.3365W
Ground Station Power = 1.5305W

## Slide 51: Teensy 4.0 Resistors
Description | Resistor | Connection
I2C SCA Pullup | 1.0-4.7 kOhm (1.0kOhm applied) | SCA to power
I2C SCL Pullup | 1.0-4.7kOhm (1.0kOhm applied) | SCL to power
APC220 TX (R1) | 1.0kOhm (brown left) | APC220 TX to Teensy 4.0 Serail2 RX (7)
APC220 TX (R2) | 2.0kOhm (red left) | APC220 TX to ground
Vout = Vin * R2/(R1 + R2)
For Vin = 5v, Vout = 3.3V: R1 = 0.5 * R2
R1 from Vin to destination
R2 is connected from Vin to ground

## Slide 52: Ground Station
Ground Station

## Slide 53: Options
Needs
  Monitor data (whole flight)
  Send data (close range) (future), bluetooth
  Wifi connection for GPS, bluetooth
Options
  Telemetry
  Bluetooth
  Wifi

## Slide 54: Architecture
Drone has telemetry receiver (and RC receiver)
Ground station has bluetooth and transmitter
  Future: use as RC transmitter also
Computer/iPhone app connects to ground station through bluetooth.

## Slide 55: Arduino Nano SPI
MISO – 12
MOSI – 11
SCK – 13
CE – 9
CSN – 10

## Slide 56: Teensy 4.0 SPI
MISO – 12
MOSI – 11
SCK – 13
CE – (4)
CSN – (2)

## Slide 57: Debugging APC220 - Teensy
Not enough power from battery through 3.3V regulator for IMU,Baro,GPS, and APC220.
  Just connecting GPS and APC220 for now
  Reset voltage regulator
Testing Enable from teensy
  Enable pin works. Setting to Sleep results in no response
Testing Set from teensy
  Automatic timeout after 5s
  Set pin works
Test RX pin on Teensy
  Able to receive through tmIO
  Able to receive through telemetryFIFO
Test TX pin on Teensy
  Write works, Nano receives a response
  Something wrong with read/write together. Nano confirms full msg is received, Teensy only sees first 2-4 bytes. FIFO problem?
  Write through tmIO, read through FIFO is GOOD. write from FIFO read from tmIO/FIFO is BAD
  Move to 200hz, consistent good results!